## Slide 1
FAPESP Advanced School on Atmospheric Aerosols IFUSP – August 1, 2019
Paulo Artaxo University of Sao Paulo, Brazil
Secondary Organic Aerosols formation in Amazonia and urban areas

## Slide 3
Swarup et al., Nature Comm, Dec 2018

## Slide 4
SOA aerosols and Clouds life cycles with ecosystem impacts

## Slide 7: Atmospheric importance of isoprene
(Adapted from Guenther et al., 2012)
January
July
Isoprene Emission
(μmol m-2 hr-1)
VOC
(isoprene, terpenes, etc.)
OH, O3
hν
Gas-phase oxidation products
Biogenic SOA
Condensation
Absorption
Reactive uptake
Notes: Isoprene (2-methyl-1,3-butadiene, C5H8) is on the global scale the non-methane volatile organic carbon (VOC) mostly emitted to the atmosphere, accounting for almost half of the world’s biogenic emissions (Guenther et al., 2012). It is the compound most abundantly emitted by vegetation in the Amazonian forest (Kuhn et al., 2010).

## Slide 8
Jimenez et al – Science 2010
World without Southern Hemisphere?
Aerosols:
1) Primary (Dust, sea salt, primary industry)
2) Secondary (SO4, NO3
3) Secondary Organic Aerosols (SOA)
Notes: Existem diversas questões em aberto com relação à produção de aerossóis orgânicos secundários

## Slide 9: Atmospheric importance of IEPOX-SOA
IEPOX-SOA = SOA derived from isoprene epoxydiols (IEPOX):
IEPOX
[Hu et al., 2015]
IEPOX-SOA factor: estimated from positive matrix factorization (PMF) of AMS organic mass spectra
Notes: So, first, what is IEPOX-SOA, and why is it important:
IEPOX-SOA is is Sec Org Aerosol derived from isoprene epoxydiols, which are known high yield products of isoprene oxidation through the HO2 pathway.
IEPOX-SOA is therefore a class of compounds, many of which are still unknown, but their contribution to organic particle mass as a whole can be estimated from AMS data, by applying the positive matrix factorization (or PMF) technique.
This estimated mass contribution is what is shown on the pie charts on this map, which show a significant percentage of this factor in regions* of high isoprene emissions and relatively low NO conditions – one of which is the Amazon forest, where isoprene is the compound most abundantly emitted by vegetation.
*in regions of the globe where the modeled gas phase IEPOX concentrations are higher, as shown by the green scale. And these regions are, accordingly,

## Slide 10
Hodzic et al. (2016)
Total emission range of global SOA: 10 to 500 Tg/year;
Degree of ABSURD uncertainty;
Generally, from 60% to 80% of the total aerosol mass is SOA
Total Global SOA Emissions Range
Notes: The SOA production budget is extremely important to global studies and in regional and global models this information is very important. In this Figure we can see that the emission range goes from ten to five hundred Teragrams per year.
So, how can the climate models predict correctly, for example, AOD, with a degree of uncertainty in a component that is generally thirty to eighty percent of the total aerosol mass.

## Slide 11
15 years ago, SOA was basically unknown information; At that time there was no necessary instrumentation.
Today in 2018, It is not explicitly included in all climate model;
Even models like WRF-Chem do not include all SOA production mechanisms (urban or remote).
Heald et al. (2005)
SOA Modeling / Simulation of Profile Evolution
Notes: Besides that, Fifteen years ago, SOA was basically unknown information and today, urban or remote SOA production mechanisms are not explicitly included in all climate models.
Perfil medido é o vermelho e o simulado é o preto. Com uma diferença de mais ou menos 80% que não se conseguia prever da massa do aerossol atmosférico.
Um exemplo disso, é que alguns anos atras quando se comparava modelo com medida errada. Naquela época não havia instrumentação necessária.
O WRF- chem gera mais SOA anthro do que biogênico, isso é fato. E ambos continuam com concentrações baixas.
em geral o SOA contribui mais do que 50% da massa. Angel encontrou q é de 17% para SP

## Slide 12
Química Atmosférica e Mudanças Climáticas
VOCs em fase gasosa: Ozônio
VOCs e produção de aerossóis secundários
Meia vida de metano controlada
pelo radical OH-
Monóxido de carbono (CO): importante no balanço de carbono
Aumento de ozônio (2010-1850) Máximo diário

## Slide 13
Production of IEPOX-derived PM from the photooxidation of isoprene
Suzane de Sá 2016

## Slide 14
From VOCs, SOA, CCN to the canopy processes in Amazonia
Fuentes et al., BAMS 2016
Notes: Figure 1. An illustra0on Of the processes Associated with biogenicvola0le Organic compound (BVOC) emissions, secondary organic Aerosol (SOA) And cloud condensa0on Nuclei (CCN) forma0on, and the setup of
Instruments used To study Photo--‐oxida0on, chemical processing, and
Transport of atmospheric cons0tuents in a remote
Amazonian rainforest.
The
ver0cal
doIed
line
represents
a
characteris0c
day0me
profile
of
virtual
poten0al
temperature
(θV(z))
and
the
horizontal
dashed
line
represents
the
top
of
the
ABL.

## Slide 15
Conceptual overview of terrestrial carbon cycle – chemistry – climate interactions
Arneth et al., 2011
Kulmala et al, 2013
Notes: The land surface aﬀects atmospheric chemistry and climate directly via surface energy partitioning into latent and sensible heat ﬂux (not shown), and emissions of greenhouse gases (H2O, CH4, N2O, CO) and aerosol particles from forests, grasslands, wetlands, agricultural systems, and vegetation biomass burning. Atmospheric chemistry and climate is also aﬀected by atmospheric reactions of reactive trace gases emitted from vegetation, soils and ﬁres (H2O, VOC, CH4, CO, NOx, NH3, H22). These contribute to complex oxidation patter ns along variable pathways that depend on the overall chemical and physical environment. Reaction kinetics vary greatly, and the lifetime of substances or their reaction products may vary from seconds (e.g., some BVOC) to years (e.g., CH) which in turn deter mines whether associated chemistry-climate eﬀects are regional or continental to global. The chief oxidizing agent is the hydroxyl radical OH, while some BVOC react directly with O3. Tropospheric humidity and hence latent heat ﬂux is an important constraint for OH formation. The main climate relevance of the atmospheric reactions is to consume or generate O, formation of secondary organic aerosol (SOA), and eﬀects on the lifetime of CH43. Climate feedbacks in the system occur directly (e.g., via the temperature and/or light response of emissions) or indirectly, for example, O
eﬀects on vegetation composition, productivity and carbon cycle.

## Slide 16
Wet Season Dry season
Air mass trajectories and footprint

## Slide 17
ATTO ACSM Monthly averages 2014-2016
Most of the nitrates are organics

## Slide 18
Organic aerosols from ATTO to Tiwa and Manacapuru (with BC)
T0a
T2
T3
Wet
Dry

## Slide 19
The organics made up to 76% of the fine particles and when investigated as a function of the scattering coefficient (σ450) different patterns (with different slopes) were observed over time. BC also shows different patterns but less pronounced
T0a ATTO - Organics versus light scattering and absorption
What drives light scattering and absorption for PM1?

## Slide 20: The hygroscopicity parameter g versus the organic mass fraction
The hygroscopicity parameter g the organic mass fraction for boreal aerosol measured in Hyytiälä, Finland (green points).
The grey show more inorganic dominated aerosol in Melpitz, Germany, during winter time.
g describes the magnitude of the scattering of enhancement factor f(RH), where f(RH)=a(1-RH)- g.
Zieger et al. (2015).

## Slide 21
  SSA decreases with aerosol ageing
    SSA decreasing trend – A clear trend of SSA decrease (stronger relative absorption) has been observed between sites, and correlating with O:C ratio. This could be result of enhanced absorption with atmospheric ageing (e.g. formation of Brown Carbon (BrC). (Joel Brito, 2019)
Optical properties versus aerosol aging – PVH, RBR, TT34

## Slide 22
Fate of isoprene RO2 radicals (ISOPO2) depicting different chemical pathways that depend on the NOx, HOx, and RO2 regimes. Several pathways lead to SOA formation, but the particle loading/composition differs greatly between different regimes, and also depends on acidic/non-acidic seeds.

## Slide 23: Influence of anthropogenic emissions on isoprene-derived particulate matter in central Amazonia
S. de Sá, et al., 2017
Observational constraints of sulfate as a first order predictor and NO as a modulator of IEPOX-derived PM.
  NOy serves as indicator of integrated exposure of airmass to NO chemistry.
  IEPOX-SOA factor obtained from PMF analysis of AMS data is a proxy for IEPOX-derived PM.
Lower loadings of IEPOX-SOA factor observed for polluted compared to background conditions

## Slide 24: The T3 research site
Intensive Operation Periods (IOPs) - 2014
IOP1: wet season IOP2: dry season
Feb 1 – Mar 31 Aug 15 – Oct 15
6/23
Notes: Site maintanined by DOE in a farm site, close to Manacapuru
A wide range of different measurements are being carried at this location, not only of aerosol particles composition and properties, but also of trace gases, meteorology, radiation, etc
I was in this trailer, which had mainly measurements for physical and chemical characterization of aerosol particles and and CCN

## Slide 25: Aerosol Mass Spectrometry
HR-ToF-AMS
[DeCarlo et al., 2006]
Mass concentrations: Organic, Sulfate, Ammonium, Nitrate, Chloride
Chemically resolved mass-size distribution
Mass spectra, EI  “fingerprint”
Aerodyne
High-resolution Time-of-Flight
Aerosol Mass Spectrometer (AMS)
Non-refractory PM1
Universal
Reproducible
Fragmentation
NR material
7/23
Notes:  for extras: know physical laws and equations for the ToF (m/z and path, etc)
Make sure to tell your routine in the field – calibrations, troubleshooting, daily checks, preliminary data analysis for first approx. QC
what is the:
  S/N ratio?
  uncertainty/error in the measurements? How calculated?
  DL?

## Slide 26
SOAS+GoAmazon: The results of the present study show that the gas-particle partitioning of approximately 100 known and newly observed oxidation products is not well explained by environmental factors (e.g., temperature). Compounds having high vapor pressures have higher particle fractions than expected from absorptive equilibrium partitioning models. Many commonly measured biogenic oxidation products may be bound in low-volatility mass that decomposes to individual compounds on analysis
SV-TAG - semi-volatile thermal desorption aerosol gas chromatograph with in situ derivatization, which provides hourly resolved concentrations and gas-particle partitioning of most common BVOC oxidation tracers
Gabriel Isaacman-VanWertz, A. Godstein EST 2016

## Slide 27
More Secondary Aerosol Potential than Expected
Palm, Jimenez, et al., GoAmazon2014/5 Special Issue
IOP1 Wet Season
IOP2 Dry Season
UTC
UTC
Results:
Secondary aerosol produced from oxidation by OH of ambient air
Production much greater than predicted from modeled yields of measured ambient precursors
Suggests that production is dominated by unmeasured species
Objective:
Test through in situ data sets the potential for secondary aerosol production and compare to state of understanding with respect to known species and their reactive yields
Predicted Formation, mg m-3
Predicted Formation, mg m-3
Measured Formation, mg m-3
Measured Formation, mg m-3

## Slide 28: Particle composition at T3
Chart: 
| Organic | Sulfate | Ammonium | Nitrate | Chloride
Sales | 79.2 | 13.1 | 4.4 | 2.5 | 0.7
79%
1%
3%
4%
13%
Chart: 
| Organic | Sulfate | Ammonium | Nitrate
Sales | 85 | 11 | 3 | 1
85%
1%
3%
11%
IOP1
(Wet season)
IOP2
(Dry season)
Organic
Sulfate
Ammonium
Nitrate Chloride
PMF
PMF
Chart: 
| IEPOX-SOA | Rest
Sales | 15 | 85
Other factors
83%
IEPOX-SOA
17%
Chart: 
| IEPOX-SOA | Rest
Sales | 15 | 85
Other factors
85%
IEPOX-SOA
15%
Notes: I am assuming that you will have already shown the location of T3 on a map before this slide.

## Slide 29: Wet season aerosol composition in central Amazonia
Manaus
Clear - T0
T3
Suzane Sá, 2018
Notes: Comparison to previous results: Chen et al., Martin et al.
- Mention org & inorg nitrate: analysis shown in supplement. Use their time series to corroborate other interpretation, but the amount of nitrate itself is small

## Slide 30: 3.2. Source apportionment of organic PM
HOA
82
53
44
60
91
55
43
(a)
Figure 3
(b)
IEPOX-SOA
MO-OOA
LO-OOA
BBOA
Fac91
57
55
41

## Slide 31: Fac 91 (parenthesis)
Cooking OA!
Bio-anthrop. SOA?

## Slide 32: Shifts in aerosols with anthrop. influences
Notes: ADD BC!!

## Slide 33: Deriving a pollution index with Cluster analysis
Conditions: afternoon (12-16 LT), no rain (10h in traj), Sol rad (4h) > 200 W m-2
Input variables: NOy, O3, logCPC, SO42-, NO3-, NH4+, Cl-, BC

## Slide 34: Shifts in PM with anthrop. influences
9 Feb 2014
13 Feb 2014
10 Feb 2014
16 Feb 2014
9 Mar 2014
8 Feb 2014
14 Mar 2014
1 h
Time scale
Suzane Sá, 2017
Notes: ADD BC!!

## Slide 35: Shifts in aerosols with anthrop. influences
Figure 5
1 h
Time scale
9 Feb 2014
13 Feb 2014
10 Feb 2014
16 Feb 2014
9 Mar 2014
8 Feb 2014
14 Mar 2014
Notes: ADD BC!!

## Slide 36: Shifts in aerosols with anthrop. influences
Figure 5
1 h
Time scale
9 Feb 2014
13 Feb 2014
10 Feb 2014
16 Feb 2014
9 Mar 2014
8 Feb 2014
14 Mar 2014
Notes: ADD BC!!

## Slide 37: Source apportionment of organic PM
(c)
Suzane Sá, 2018

## Slide 38: Source apportionment of organic PM – AMS + SV-TAG + PTR+ Others
IEPOX-SOA
MO-OOA
LO-OOA
BBOA
Fac91
HOA
AMS
SV-TAG
PTR-MS
Other
Suzane Sá, 2018
Notes: ADD BC!!

## Slide 39: Shifts in aerosols with anthrop. influences
  Increase in organic aerosols from 0.7 to 4 ug/m³
Clean Regional Small pollution Heavy pollution
Notes: ADD BC!!

## Slide 40
SOA production in Amazonia DRY season

## Slide 41: 3.3. Shifts in PM with anthrop. influences
Notes: ADD BC!!

## Slide 42
A very dynamic system with the interaction of the Manaus plume with the background air
Large temporal and spatial variability: a challenge for the models
Rahul Zaveri et al., 2018

## Slide 43
Transverse Transects of Urban Plume
500 m, 11 AM local, 13 March 2014
Data Sources: Mei Fan, Stephen Springston, IARA Experiment, DOE AAF G1 Platform

## Slide 44
Box and whisker representations of the G-1 AMS data for both the wet and dry seasons (top panel), average particle chemical composition for each flight (middle panel), and average aerosol chemical composition for all flights (bottom).

## Slide 45
Time traces of relevant quantities on March 13th, 2014 flight. AMS data uses the HR-analysis routine described in the literature to minimize interferences (Aiken et al., 2007). Note the mass of inorganic species (SO4, NO3, NH4) has been multiplied by a factor of five to improve the figure clarity. PTR-MS signal at m/z 69 corresponds to isoprene, m/z 71 corresponds to the sum of methylvinyl ketone (MVK), methacrolein (MACR), and isoprene hydroxyhydroperoxide (ISOPOOH), all oxidation products of isoprene, and m/z 79 corresponds to benzene.

## Slide 46
PMF analysis of the organic aerosol on the March 13th 2014 flight. The PMF analysis utilized the high resolution dataset. All data from the wet season were included in the analysis.

## Slide 47
Shrivastava et al., Nature Comm 2019

## Slide 48
Fig.1. (a) OA measured along aircraft flight transects at 500-m altitude on March 13 (orange) and model-predicted OA, as described in the text. (b) Measured and model predicted average percent enhancement in plume compared to background organic aerosol on 4 different flight transects, as marked in (a). Bars represent measurements while symbols represent a model-predicted increase of OA within Manaus plume compared to background conditions
WRF-Chem simulations showing (a) Biogenic SOA when all emissions are on (b) Biogenic SOA when biogenic VOC emissions are on but Manaus emissions are turned off (c) Biogenic SOA enhancement factor calculated as the ratio of two simulations with Manaus emissions turned on/off i.e. (a)/(b). WRF-Chem predictions are at ~500 m altitude, averaged during the afternoon (16-20 UTC = 12-16 local time) of March 13, 2014.

## Slide 49
Fig. 3. WRF-Chem simulated concentrations of NOx (ppbv), O3 (ppbv) and OH (106 molecule cm- 3) for an altitude of ~500 m, averaged during the afternoon (16-20 UTC) of March 13, 2014. Top panels show simulations with all emissions on, while bottom panels show simulations with biogenic emissions on but Manaus emissions off. A comparison of top and bottom panels demonstrates how NOx and oxidants are greatly enhanced by the Manaus plume within the otherwise pristine Amazon
Aircraft-measured and WRF-Chem simulated median values of absolute OA concentrations in-plume and at background locations. Calculations are shown for individual flight transects on 13 March 2014, since the aircraft clearly identified the plume evolution on this day, as described in the text. An Average across all flight transects is shown for March 14 and 16, and the modeled plume was determined by scanning all radial locations downwind T1 site

## Slide 50: How particles are produced in Amazonia?
T0 site (ATTO)
(All data)
N: ~320 cm-3
UTC
Feb. 1- Mar. 31, 2014
Day time
UTC
Day time
T0 site (ATTO)
(dry season)
N: ~3100 cm-3
It rains a lot. Removal very high. How the particles are formed?

## Slide 51: Central Questions
What controls the lifecycle – especially the sources – of aerosols in the pristine atmosphere?
How do secondary aerosol particles originate?
What is the role of nucleation “banana” events?
(Kerminen et al., 2012)

## Slide 52
Andi Andreae, 2016
Andi Andreae, Schneider, in prep 2016
AMS Aerosol composition: Organics and nitrates. No sulfates

## Slide 53: Aging of organic aerosol – AC 13 Altitude & f82 dependence
Fresher organics at high altitudes
with high f82

## Slide 54
IEPOX tracer f82 against R44/43 for the lower troposphere (dark green, LT) and upper troposphere (light green, UT).
High altitude aerosols are fresh and mostly IEPOX derived…

## Slide 55
Biogenic organic aerosol formation at low H2SO4 happens in UT!
Was this the dominant mechanism in the pristine atmosphere before the advent of air pollution?

## Slide 56
Clouds as active aerosol processors in the atmosphere

## Slide 57: Convective precipitation brings these particles down to the surface
Wang et al. (2016, in press)

## Slide 58
Thanks for the attention!!!!

## Slide 59
Free data police: All GoAmazon data is freely available at the DoE ARM site and in our Brazilian database
Thanks for the attention!!

## Slide 60: Aerosol Hygroscopicity
T2
T0
T3
Pöhlker et al., Thalman et al., Barbosa et al., in prep
Results: Dominated by organics, with very low hygroscopicity; Manaus plume affects the Aitken mode, oxidized T2->T3
Notes: DATA:
T0= average of the whole year
T2= Polluted is just Feb/2015 (hence only manaus, no biomass burning); T2/BB is Sep/15 until Oct/15 2014 (that month of high BB regional)
T3= Ryan’s criteria to separate, all year, into the three classifications.
What I see here:
Background => T0/ATTO and T3-Clean agree with preivous campaign (Gunthe)
Pollution => T2 is lower than T3-polluted only for small particles (<=100nm). They should grow
Biomass Burning=> I don’t understand why T2 is lower than T3 for small sizes. If the Manaus plume (higher values) is mixed with the BB, the results should be more higroscopicity, right??

## Slide 61
Isoprene Chemistry over the Amazon Rain Forest
Liu, Artaxo, Martin et al., PNAS
NO
HO2
OH
Isoprene
ISOPOOH
Isoprene-derived
hydroperoxides
…
MVK
Methyl vinyl ketone
MACR
Methacrolein
…
Observational constraints of anthropogenic influence.
Underestimate of the NO pathway for background conditions.
Anthropogenic Pollution
Bkgd
Observations
[ISOPOOH]
[MVK] + [MACR]
CTM prediction
ppb NOy

## Slide 62: Aerossóis Carbonáceos
Responsáveis por >70% da massa de aerossol na Amazônia;
Diferentes tipos de aerossóis carbonáceos:
  Carbono orgânico (OC):
    refere-se ao carbono presente em compostos majoritariamente orgânicos;
    pode ser primário ou secundário (SOA);
  Carbono elementar (EC):
    Fração de carbono com composição similar à fuligem;
    Altamente absorvedor de radiação;
  Black Carbon (BCe):
    Carbono altamente absorvedor de luz com propriedades ópticas semelhantes às da fuligem.
US EPA
Notes: Não falar em medição
Black carbon (BC), produced during incomplete fossil-fuel and biomass combustion processes, is one of the major absorbing particulate species in the atmosphere
The variability in MAE has been interpreted in terms of source regions, analytical measurement protocols, chemical and optical properties of aerosols at a sampling site

## Slide 63
Isoprene Photochemistry in Transition?
NO
HO2
RO2
Isomerization
OH
Isoprene
ISOPOO
Products
Products
ISOPOOHs
(C5H10O3)
…
methyl vinyl ketone
(MVK, C4H6O)
methacrolein
(MACR, C4H6O)
…
(Tuazon et al., 1990; Paulot et al., 2009; Surratt et al., 2010; Crounse et al., 2011,
Peeters et al., 2009; 2010; 2014; Fuchs et al., 2013…)
Harvard University Environmental Chemistry Group
Notes: In this study we tried to approach this question of anthropogenic influence by directly measuring the concentrations of their respective major products over Amazonia under both clean and polluted conditions. MVK, MACR are major products of NO pathway and ISOPOOH is the major products of HO2 pathway.

## Slide 64: Amazonia: Liquid Organic Particulate Matter Aerosols are part of the liquid atmosphere (not the solid one)…
Adam Bateman (2016)
Liquid
Solid

## Slide 65
Image Source: Jerome Fast
Pöschl, et al., Science, 2010
How external (Biomass Burning, Sahara dust, pollution) and internal emissions (primary organic aerosol particles and SOA) interact chemically and physically altering aerosol and cloud properties.
2 years continuous measurements at seven ground based stations and two aircraft flying dry and wet seasons

## Slide 66
T0z: Scattering versus organics