## Slide 1: Characteristics of aerosols from pristine and biomass burning impacted regions in Amazonia
Paulo Artaxo, Henrique Barbosa, Luciana Rizzo, Joel Brito, Andrea Arana, Rafael Stern, John Backman, Andi Andreae, Christopher Pohlker, Xuguang Chi, Jorge Saturno and others
Acridicon Science Meeting, São José dos Campos, May 21, 2014

## Slide 2
Amazonia: 3 types of aerosol particles
Biogenic (primary and SOA)
Biomass Burning
Dust from Sahara
Each with VERY different properties and impacts
Size: from 1 nanometer to 10 micrometers

## Slide 3
Qi Chen, submitted 2014

## Slide 4
Maximum monthly, annual mean and minimum monthly mean Amazon river discharge at Óbidos and in green maximum and minimum daily mean river discharge, (Gloor et al. GRL 2013).
Is the Amazonian hydrological cycle intensifying?
Tropical Atlantic sea surface temperature

## Slide 5
Rain rate (TRMM) versus Aerosol Optical Depth (MODIS)
13:30 local-time map of rain rate (R) and the observed trend with aerosol loading in four selected regions. Period: July and August 2007. b, The average R values are plotted for six aerosol-loading sets (blue, including zero R grid squares; red, without zero R grid squares). Note the R intensification as a function of AOD in all cases. (Koren et al., Nature 2012)
Amazonia

## Slide 6
Relationship between aerosols and precipitation in the La Plata Basin
AERONET (Aerossols) +
TRMM (Precipitation) + BRAMS (simulations)
Reduction in precipitation with increase in aerosols
Silva Dias et al., 2014
BRAMS: Simulations with cloud microphysics confirm the measurements

## Slide 7
Manaus aerosol and trace gas measurements

## Slide 8
500 m - May
500 m November
Manaus Footprint
Manaus Footprint
Air Mass Trajectories (10 days) and Footprint

## Slide 9: Aerosol Optical Thickness in Manaus – 2000-2009 MODIS 550 nm
(b)
Wet Season
Dry Season

## Slide 10
Espessura ótica de aerossóis em 550 nm 1999-2012 em Porto Velho, Rondonia

## Slide 11
ZF2 Time series of black carbon fine and coarse mode
Chart: Manaus ZF2 SFU - Black Carbon fine and coarse mode concentration
Chart: Ratio Black Carbon / Aerosol Mass

## Slide 12
Chart: Porto Velho fine and coarse mode aerosol mass 1999-2012
Chart: Porto Velho Black Carbon 2009-2012 Fine and Coarse Mode
Porto Velho fine and coarse mode aerosol mass concentration and black carbon from 1999 to 2012

## Slide 13: Scattering and absorption daily median comparison (2008-2014)
All data corrected for STP (1013.25 mbar, 0C).
Notes: Dry season: ATTO and TT34 are very similar (regional biomass burning emissions dominate particle optical properties).
Wet season: occasional differences between ATTO and TT34. All data corrected for STP (1013.25 mbar, 0oC). Scattering corrected for truncation error.

## Slide 14: Single scattering albedo and scattering angstrom daily median comparison (2008-2014)
Notes: Wet season: Single Scattering Albedo and Angstrom exponent are noisier at both sites, partly due to low aerosol loadings and prevailance of coarse mode particles. All data corrected for STP (1013.25 mbar, 0oC). Scattering corrected for truncation error.

## Slide 15
ZF2 daily medians of particle number concentrations integrated from observed size distributions (10-600 nm).
Rizzo et al., submitted 2014
N=103,472
spectra

## Slide 16
Chart: Dry season
| 10.7 | 12.4 | 14.5 | 16.899999999999999 | 19.7 | 23 | 26.9 | 31.5 | 36.9 | 43.3 | 50.9 | 60 | 70.8 | 83.8 | 99.5 | 118.8 | 142.4 | 171.8 | 208.7 | 255.7 | 316.10000000000002 | 394.8 | 498.4 | 635.4
0:00-6:00 | 0 | 0 | 19.868 | 50.9153 | 87.501 | 133.9819 | 187.8348 | 270.1391 | 391.934 | 558.2489 | 794.539 | 1141.0386 | 1499.8003 | 1756.601 | 1980.9477 | 2304.0255 | 2466.014 | 2282.7785 | 1773.9057 | 1129.863 | 587.927 | 223.56 | 56.4655 | 10.7852
6:00-14:00 | 0 | 0.0014849 | 20.7665 | 39.4173 | 57.895 | 80.9332 | 109.8761 | 157.7408 | 229.8441 | 351.2958 | 563.5105 | 890.5218 | 1291.6477 | 1620.1321 | 1922.0236 | 2340.3626 | 2603.2063 | 2515.1884 | 1959.5692 | 1307.0668 | 696.9122 | 265.424 | 69.2367 | 14.4277
14:00-18:00 | 0 | 14.8256 | 30.3706 | 48.9206 | 63.9231 | 81.9215 | 105.7738 | 150.43 | 223.4321 | 336.505 | 527.6882 | 820.5874 | 1189.4322 | 1493.4908 | 1801.1058 | 2284.4665 | 2634.4968 | 2550.1219 | 1994.8918 | 1329.4598 | 739.0627 | 280.9471 | 71.2473 | 14.992
18:00-24:00 | 0 | 18.0353 | 48.1821 | 79.4441 | 115.305 | 154.5404 | 203.467 | 278.3799 | 393.1511 | 557.2043 | 790.7838 | 1113.8598 | 1451.9887 | 1684.697 | 1925.7364 | 2272.1705 | 2512.2654 | 2383.7603 | 1862.8631 | 1202.7581 | 654.186 | 255.2627 | 63.3585 | 12.2742
Chart: Wet season
| 10.7 | 12.4 | 14.5 | 16.899999999999999 | 19.7 | 23 | 26.9 | 31.5 | 36.9 | 43.3 | 50.9 | 60 | 70.8 | 83.8 | 99.5 | 118.8 | 142.4 | 171.8 | 208.7 | 255.7 | 316.10000000000002 | 394.8 | 498.4 | 635.4
0:00-6:00 | 0 | 5.3347 | 39.6395 | 81.1525 | 119.0268 | 151.2028 | 182.8689 | 214.8352 | 256.5289 | 320.6299 | 422.306 | 555.6954 | 660.0337 | 658.8319 | 569.5013 | 512.4216 | 516.7751 | 469.7159 | 342.4538 | 193.7953 | 83.4099 | 28.6127 | 3.8351 | 0.45904
6:00-14:00 | 0 | 0.0030273 | 25.6858 | 53.1497 | 78.2694 | 102.8558 | 128.491 | 159.8809 | 206.041 | 265.1174 | 359.7951 | 489.4794 | 640.6999 | 657.1234 | 592.6947 | 585.7892 | 615.3071 | 592.4981 | 480.3641 | 297.652 | 139.0141 | 48.4145 | 6.8064 | 0.81106
14:00-18:00 | 0 | 11.0937 | 35.4234 | 56.1228 | 73.1514 | 87.2841 | 100.873 | 124.1588 | 163.8406 | 219.7728 | 310.9185 | 443.1896 | 548.3775 | 558.5246 | 534.1967 | 582.1992 | 645.3472 | 620.5121 | 505.7403 | 319.0819 | 160.4824 | 61.1958 | 9.6657 | 1.2417
18:00-24:00 | 0 | 20.1022 | 61.2179 | 103.0908 | 133.4306 | 153.2155 | 172.9693 | 197.7438 | 235.22 | 287.3434 | 384.9724 | 523.5892 | 638.2491 | 654.1092 | 575.1426 | 539.9357 | 569.9067 | 542.6315 | 435.6281 | 268.5112 | 123.992 | 47.3301 | 6.9906 | 0.88832
Median particle number size distributions considering different periods of the day for wet and dry seasons. (Local time)
Rizzo et al., submitted 2014

## Slide 17
Size distribution Wet Season
Secondary Organic Aerosol
Primary
Biological
Particles
BB/SOA
Dry Season
AERONET size distribution similar with ground based SMPS
PBP
AERONET size distributions

## Slide 18: A zoom in the dry season (Jul-Oct 2013)
Light scattering

## Slide 19: A zoom in the dry season (Jul-Oct 2013)
Black Carbon

## Slide 20: A zoom in the wet season (Scattering, Absorption and SSA)

## Slide 21
Monthly statistics (2009 – 2012) for light scattering coefficient σs at 637 nm and light absorption coefficient σa at 637 nm in Mm-1 for Porto Velho (PVH, in black) and central Amazonia (TT34, in red).
Single Scattering Albedo Lower at the pristine site
Scattering, absorption and SSA in Manaus and Porto Velho
Artaxo et al., 2013

## Slide 22
Adapted from Zhang et al., Geophys. Res. Lett., 2007 and Chen et al. Geophys. Res. Lett., 2009, 36, L20806.
Amazon
0.6 µg m-3
Organic compounds are major component of atmospheric aerosol, specially in Amazonia

## Slide 23
ACSM at ATTO: Time series wet season
Feb-Mar 2014
Notes: Medidas iniciaram no meio de Fevereiro e ocorrem continuamente. Valores normalmente baixos (<1ug m-3). Detalhe para aumento significativo de cloreto, identificado como transporte de sal marinho. O ruído na medida de sal marinho é pelo fato de demorar para evaporar no vaporizador, causando problemas na subtração do branco.

## Slide 24
ACSM at ATTO: Comparing SMPS with sum ACSM+EBC
Notes: Comparação início da amostragem entre aetalômetro, SMPS e ACSM

## Slide 25
ACSM at ATTO: Diurnal variability
Notes: Mediana das concentrações observadas durante 40 dias de amostragem. Interessante o primeiro pico da parte da manhã, acompanhando Org, SO4 e NO3, e um segundo na tarde, só de orgânicos. Cuidado com concentrações de NO3, em interferencia com orgânicos que ainda tem que ser tratado.

## Slide 26
ACSM at ZF2: Dry season July-Dec 2013

## Slide 27
Manaus ACSM 2013 wet season measurements
PM1~0.61 µg/m³

## Slide 28
A highly oxidized aerosol at ZF2 (July-Dec 2013) and ATTO (Jan-Mar 2014)
ZF2
ATTO
f44 = mainly CO2+, an indicator of highly oxidized species
f43 = mostly due to C2H3O+, an indicator of less oxidized species.

## Slide 29
f44 = mainly CO2+, an indicator of highly oxidized species
f43 = mostly due to C2H3O+, an indicator of less oxidized species.
SAMBBA Biomass Burning f44/f43 plot ACSM

## Slide 30
Manacapuru
Aug, 18 - Sept 1, 2013
f44 = mainly CO2+, an indicator of highly oxidized species
f43 = mostly due to C2H3O+, an indicator of less oxidized species.

## Slide 31
Submicron non-refractory aerosol composition at the PVH site
Joel de Brito, 2013

## Slide 32
Qi Chen, submitted 2014
Diurnal variability of aerosol species in Amaze

## Slide 33
AMAZE 2008 PMF Results of the submicron fraction of the wet season Amazonian aerosol
1) HOA: The HOA factor was interpreted as representing regional and local pollution and accounted for 14% of the organic particle mass concentration.
2) OOA-1: Accounts for 14% of the organic particle mass concentration, was highly oxidized and plausibly related to long-range transport of African biomass burning particles.
3) OOA-2: Tied to the production of biogenic SOM and together with OOA-3 accounted for >70% of the organic particle mass concentration. This factor was consistent with the reactive uptake of isoprene oxidation products such as IEPOX by acidic aerosol particles, including haze, fog, and cloud droplets. OOA-2 factor was associated with sustained particle-phase SOM production.
4) OOA-3: Had mass spectral features of freshly formed biogenic SOM, believed to represent gas-to-particle condensation followed by oxidation of gas-phase BVOCs. OOA-3 factor was associated with sporadic, episodic SOM production by processes of gas-to-particle conversion
Qi Chen, submitted 2014

## Slide 34
Time series of the fractional contribution by each of the four statistical factors identified by PMF analysis in AMAZE
Qi Chen, submitted 2014

## Slide 35
ZF2 time series of organic and elemental carbon
Chart: Manaus ZF2 - Concentração OC, EC e TC (ug m-3)
Chart: Wet
| OC/TC | EC/TC
Wet | 0.9512 | 0.048797
Chart: 
| OC/TC | EC/TC
Dry | 0.92834 | 0.071648
Elemental Carbon is very low…

## Slide 36
Positive Matrix Factorization (PMF) profiles of fine and coarse total carbon factors
Standard thermograms
Gilardoni et al., 2011
Coarse Mode
Fine Mode
Wet season carbon fraction fine mode:
BB: 35%
SOA: 49%
Dry season:
BB: 71%
SOA: 25%
F1: SOA
F2: BB
F3: Volatiles
F1: SOA
F2: PBAP
F3: Fungi

## Slide 37
Thanks for the attention!!!

## Slide 38
Porto Velho SAMBBA ACSM H:C and O:C and oxidation state

## Slide 39
Cloud base height: Raman Lidar versus ceilometer at EMBRAPA
Analysis by Henrique Barbosa and Elisa Sena

## Slide 40: Main issues
Explore more intensively links between forest biology and aerosols for fine and coarse modes (PBAP, SOA)
CCN population: composition and size role on cloud droplet activation.
Explore links between VOCs and SOA aerosols
Brown carbon: Design a strategy to quantify the contribution of brown carbon to aerosol absorption
Investigate oxidation states of organic aerosols and associate with aerosol dynamics
Many other issues…

## Slide 41
Termograms showing the types of carbon present in atmospheric aerosol in Porto Velho and ZF2
ZF2

## Slide 42
Night time bursts of 20-40 nm particles: 70% of the time
ZF2

## Slide 43
Night time bursts of 20-40 nm particles: 70% of the time

## Slide 44
Chart: Ozone [ppb]
Chart: TT34 median diurnal cycle (2009-2012)
| 2.0833333000000006E-2 | 4.1666666999999998E-2 | 6.25E-2 | 8.3333333000000023E-2 | 0.10416667000000003 | 0.125 | 0.14583333000000004 | 0.16666666999999996 | 0.18750000000000003 | 0.20833333000000004 | 0.22916666999999996 | 0.25 | 0.27083332999999998 | 0.29166667000000007 | 0.31250000000000006 | 0.33333333000000004 | 0.35416667000000007 | 0.37500000000000006 | 0.39583333000000004 | 0.41666667000000007 | 0.43750000000000006 | 0.45833332999999998 | 0.47916667000000007 | 0.5 | 0.52083332999999987 | 0.54166667000000002 | 0.5625 | 0.58333332999999976 | 0.60416667000000002 | 0.62500000000000011 | 0.64583332999999998 | 0.66666667000000013 | 0.6875 | 0.70833332999999987 | 0.72916667000000002 | 0.75000000000000011 | 0.77083332999999998 | 0.79166667000000002 | 0.8125 | 0.83333332999999987 | 0.85416667000000002 | 0.87500000000000011 | 0.89583332999999987 | 0.91666667000000002 | 0.9375 | 0.95833332999999987 | 0.97916667000000002 | 1
wet season | 2.89 | 2.815 | 2.73 | 2.51 | 2.5 | 2.33 | 2.25 | 2.22 | 2.38 | 2.43 | 2.21 | 2.22 | 2.145 | 2.215 | 2.26 | 2.65 | 3.46 | 4.17 | 5.11 | 6.15 | 6.81 | 7.38 | 7.575 | 7.89 | 8.175 | 8.3 | 8.31 | 8.25 | 8.28 | 7.94 | 7.8 | 7.69 | 7.375 | 7.09 | 6.66 | 6.28 | 5.58 | 5.08 | 4.51 | 4.32 | 4.08 | 3.85 | 3.78 | 3.755 | 3.58 | 3.38 | 3.19 | 2.99
dry season | 7.75 | 7.33 | 7.3 | 7.005 | 6.395 | 6.06 | 5.895 | 5.81 | 5.64 | 5.22 | 5.005 | 4.865 | 4.73 | 4.69 | 4.76 | 5.82 | 7.13 | 8.42 | 9.65 | 10.995 | 12.385 | 13.005 | 13.96 | 14.51 | 14.72 | 15.22 | 15.305 | 15.59 | 15.635 | 15.99 | 15.825 | 15.495 | 15.13 | 14.4 | 13.755 | 13.08 | 12.37 | 11.66 | 11.03 | 10.87 | 10.69 | 10.36 | 10.165 | 9.69 | 8.99 | 8.93 | 8.51 | 8.17
O3 at ZF2

## Slide 45
Median particle absorption spectrum at the ATTO site, for 2012-2013 dry and wet season data. Dashed line shows a typical absorption spectrum of black carbon particles, with AAE=1.0 (Absorption Angstrom Exponent). Aethalometer data were corrected for filter loading and multiple scattering effects.
Particle absorption spectrum at ATTO

## Slide 46
Chart: Avg30min CO [ppm]
CO at ZF2 (Picarro)
Chart: CO ZF2 Average diurnal cycle
| 2.0829166999999999E-2 | 4.1662431000000014E-2 | 6.2495694000000011E-2 | 8.3328958000000022E-2 | 0.10416222000000003 | 0.12499549000000001 | 0.14582875000000001 | 0.16666201 | 0.18749528000000001 | 0.20832854000000001 | 0.22916180999999997 | 0.24999507000000004 | 0.27082833000000006 | 0.29166160000000002 | 0.3124948600000001 | 0.33332812000000012 | 0.35416139000000002 | 0.37499465000000004 | 0.39582792000000011 | 0.41666118000000002 | 0.43749444000000004 | 0.45832771000000005 | 0.47916097000000007 | 0.49999424000000003 | 0.5208275 | 0.54166075999999996 | 0.56249402999999998 | 0.58332728999999994 | 0.60416055999999996 | 0.62499382000000014 | 0.64582708000000011 | 0.66666035000000012 | 0.68749360999999998 | 0.70832687999999999 | 0.72916013999999996 | 0.74999340000000014 | 0.77082667000000016 | 0.79165993000000012 | 0.81249318999999987 | 0.83332645999999999 | 0.85415972000000007 | 0.87499298999999997 | 0.89582625000000005 | 0.91665951000000012 | 0.93749277999999991 | 0.95832603999999999 | 0.97915931000000012 | 0.99999256999999986
Dec-2010 | 0.13767 | 0.13881 | 0.13915 | 0.1401 | 0.14237 | 0.14568 | 0.14549 | 0.14767 | 0.14726 | 0.14772 | 0.14794 | 0.14852 | 0.14901 | 0.14711 | 0.1449 | 0.14302 | 0.13909 | 0.13589 | 0.13289 | 0.13166 | 0.13077 | 0.13001 | 0.13053 | 0.12991 | 0.13081 | 0.13057 | 0.13013 | 0.13052 | 0.13044 | 0.12929 | 0.13038 | 0.12964 | 0.12811 | 0.12719 | 0.12699 | 0.12723 | 0.12747 | 0.12789 | 0.12805 | 0.1283 | 0.12913 | 0.12957 | 0.13015 | 0.13092 | 0.13216 | 0.13371 | 0.13422 | 0.13463
Jan-2011 | 0.12081 | 0.12159 | 0.1222 | 0.12299 | 0.12304 | 0.12335 | 0.12444 | 0.12492 | 0.1251 | 0.12528 | 0.12618 | 0.12714 | 0.12743 | 0.12715 | 0.12641 | 0.12484 | 0.1221 | 0.1188 | 0.11701 | 0.11633 | 0.11606 | 0.11563 | 0.11527 | 0.11512 | 0.11521 | 0.11538 | 0.11529 | 0.11445 | 0.11442 | 0.11373 | 0.11274 | 0.11272 | 0.11264 | 0.11276 | 0.1134 | 0.1142 | 0.11449 | 0.11462 | 0.11489 | 0.1152 | 0.11545 | 0.11657 | 0.1174 | 0.11748 | 0.11763 | 0.11909 | 0.11941 | 0.12002
Feb-2011 | 0.12166 | 0.1222 | 0.12246 | 0.12349 | 0.12418 | 0.1249 | 0.12698 | 0.1279 | 0.12846 | 0.12968 | 0.13033 | 0.13074 | 0.1306 | 0.13049 | 0.12999 | 0.12776 | 0.1255 | 0.12265 | 0.12 | 0.11856 | 0.11866 | 0.11856 | 0.11827 | 0.11808 | 0.11799 | 0.11777 | 0.11747 | 0.11732 | 0.117 | 0.11558 | 0.11507 | 0.11532 | 0.11548 | 0.11465 | 0.11469 | 0.11469 | 0.11507 | 0.11549 | 0.117 | 0.11813 | 0.11884 | 0.11987 | 0.12042 | 0.12027 | 0.12069 | 0.12113 | 0.12118 | 0.12146
Mar-2011 | 0.11868 | 0.11899 | 0.12 | 0.12102 | 0.12331 | 0.12591 | 0.12768 | 0.12696 | 0.12684 | 0.12627 | 0.12537 | 0.12538 | 0.12544 | 0.12582 | 0.12536 | 0.12357 | 0.12013 | 0.11748 | 0.11385 | 0.1143 | 0.11433 | 0.11357 | 0.11408 | 0.11394 | 0.11479 | 0.11457 | 0.11511 | 0.11467 | 0.1139 | 0.11325 | 0.11234 | 0.11168 | 0.11201 | 0.11189 | 0.11193 | 0.11243 | 0.11282 | 0.11267 | 0.11237 | 0.11287 | 0.11303 | 0.1131 | 0.11392 | 0.11431 | 0.11577 | 0.11699 | 0.11742 | 0.1179
Apr-2011 | 0.11309 | 0.11413 | 0.11495 | 0.11571 | 0.11625 | 0.11734 | 0.11727 | 0.1182 | 0.11902 | 0.12023 | 0.12107 | 0.12647 | 0.12441 | 0.12455 | 0.12281 | 0.11836 | 0.11415 | 0.11011 | 0.10864 | 0.10482 | 0.10547 | 0.10752 | 0.10833 | 0.10903 | 0.10912 | 0.10846 | 0.10778 | 0.1073 | 0.108 | 0.1075 | 0.10684 | 0.10627 | 0.10592 | 0.10579 | 0.10568 | 0.10551 | 0.10552 | 0.10668 | 0.10716 | 0.10794 | 0.10834 | 0.10933 | 0.11008 | 0.11043 | 0.11102 | 0.11142 | 0.11204 | 0.1126
May-2011 | 0.099928 | 0.10059 | 0.10119 | 0.10165 | 0.10277 | 0.10364 | 0.10409 | 0.10435 | 0.10555 | 0.10615 | 0.10716 | 0.1086 | 0.10873 | 0.10882 | 0.10818 | 0.10757 | 0.10367 | 0.099046 | 0.092371 | 0.088545 | 0.08892 | 0.08775 | 0.089407 | 0.091529 | 0.092745 | 0.092253 | 0.091071 | 0.091032 | 0.089754 | 0.089084 | 0.089854 | 0.090246 | 0.090453 | 0.087562 | 0.087317 | 0.087292 | 0.08804 | 0.089387 | 0.089941 | 0.091231 | 0.092372 | 0.094919 | 0.094917 | 0.096747 | 0.09648 | 0.096818 | 0.09799 | 0.097401
Jun-2011 | 0.10201 | 0.10336 | 0.10409 | 0.10436 | 0.10482 | 0.10646 | 0.10691 | 0.10615 | 0.10709 | 0.10704 | 0.10663 | 0.10854 | 0.10934 | 0.11071 | 0.11164 | 0.10951 | 0.10481 | 0.099791 | 0.095542 | 0.092131 | 0.09015 | 0.091394 | 0.092893 | 0.09598 | 0.097588 | 0.098409 | 0.099509 | 0.10106 | 0.10057 | 0.099844 | 0.098879 | 0.099558 | 0.099238 | 0.097879 | 0.096879 | 0.096154 | 0.096623 | 0.097816 | 0.098608 | 0.098803 | 0.09957 | 0.10022 | 0.10114 | 0.10163 | 0.1028 | 0.10264 | 0.10175 | 0.10135

## Slide 47
 | Dry Season |  |  |  |  |  |  |  | Wet Season |  |  |  |  |  |  | 
 | Fine Mode |  |  | N | Coarse Mode |  |  | N | Fine Mode |  |  | N | Coarse Mode |  |  | N
PM | 7356 | ± | 4238 | 39 | 6072 | ± | 2490 | 39 | 2006 | ± | 1357 | 63 | 7792 | ± | 4536 | 58
BC | 574 | ± | 380 | 39 | 51 | ± | 21 | 39 | 154 | ± | 152 | 63 | 66 | ± | 33 | 58
Na | 61 | ± | 43 | 22 | 63 | ± | 42 | 23 | 21 | ± | 19 | 32 | 63 | ± | 65 | 36
Mg | 13 | ± | 8.5 | 19 | 21 | ± | 13 | 27 | 20 | ± | 26 | 38 | 24 | ± | 25 | 48
Al | 30 | ± | 22 | 39 | 39 | ± | 28 | 39 | 69 | ± | 112 | 48 | 62 | ± | 95 | 58
Si | 31 | ± | 19 | 39 | 52 | ± | 33 | 39 | 124 | ± | 190 | 48 | 125 | ± | 184 | 58
P | 12 | ± | 5.7 | 39 | 20 | ± | 14 | 39 | 4.3 | ± | 2.5 | 48 | 34 | ± | 19 | 58
S | 346 | ± | 160 | 39 | 62 | ± | 28 | 39 | 106 | ± | 70 | 48 | 54 | ± | 32 | 58
Cl | 4.0 | ± | 3.4 | 19 | 28 | ± | 22 | 39 | 4.0 | ± | 4.5 | 32 | 83 | ± | 115 | 58
K | 184 | ± | 121 | 39 | 70 | ± | 34 | 39 | 45 | ± | 42 | 48 | 101 | ± | 54 | 58
Ca | 6.8 | ± | 3.8 | 39 | 17 | ± | 9 | 39 | 11 | ± | 18 | 48 | 25 | ± | 32 | 58
Ti | 1.9 | ± | 1.1 | 39 | 4.4 | ± | 2.7 | 39 | 4.1 | ± | 5.6 | 43 | 4.7 | ± | 6.3 | 58
V | 0.4 | ± | 0.4 | 15 | 0.3 | ± | 0.2 | 17 | 0.5 | ± | 0.7 | 25 | 0.2 | ± | 0.2 | 26
Cr | 0.5 | ± | 0.6 | 23 | 0.4 | ± | 0.3 | 27 | 0.4 | ± | 0.4 | 28 | 0.5 | ± | 0.6 | 46
Mn | 0.6 | ± | 0.6 | 39 | 0.4 | ± | 0.2 | 33 | 0.7 | ± | 0.7 | 45 | 0.9 | ± | 0.9 | 58
Fe | 16 | ± | 9.6 | 39 | 28 | ± | 15 | 39 | 31 | ± | 49 | 48 | 37 | ± | 52 | 58
Ni | 0.4 | ± | 0.5 | 31 | 0.1 | ± | 0.2 | 17 | 0.4 | ± | 0.4 | 43 | 0.2 | ± | 0.2 | 33
Cu | 1.3 | ± | 4.6 | 30 | 0.5 | ± | 0.8 | 33 | 0.3 | ± | 0.6 | 41 | 0.3 | ± | 0.3 | 58
Zn | 1.7 | ± | 1.0 | 39 | 0.8 | ± | 0.4 | 39 | 0.5 | ± | 0.3 | 48 | 0.9 | ± | 0.5 | 58
Br | 1.3 | ± | 0.8 | 39 | 0.5 | ± | 0.4 | 24 | 0.5 | ± | 0.6 | 34 | 0.4 | ± | 0.4 | 41
Rb | 0.8 | ± | 1.3 | 12 | 0.6 | ± | 0.6 | 8 | 0.6 | ± | 0.9 | 16 | 0.5 | ± | 0.5 | 21
Sr | 2.5 | ± | 2 | 4 | 2.2 | ± | 0 | 1 | 1 | ± | 0.3 | 2 | 1.6 | ± | 2 | 6
Pb | 1.6 | ± | 2.3 | 21 | 1.4 | ± | 1.5 | 14 | 0.9 | ± | 0.9 | 24 | 0.7 | ± | 0.9 | 23
EBC/PM (%) | 7.5 | ± | 1.8 | 39 | 1 | ± | 0.4 | 39 | 8.2 | ± | 4.1 | 63 | 0.9 | ± | 0.2 | 63
SO4/PM10 (%) | 15 | ± | 4 | 39 | 3.3 | ± | 1.2 | 39 | 17 | ± | 5 | 63 | 2.1 | ± | 0.5 | 63
Elemental composition of aerosols at ZF2

## Slide 48
MAAP Standard MAC: 6.6 m2 g-1
MAC = 4.7 m2 g-1 em 637nm
Petzold and Schomlinner (2004) = 7.8 – 9.2 m2 g-1
Linear fit of MAAP light absorption coefficient (Babs) and thermal-optical EC concentration (red); the black line corresponds to the absorption cross section of 6.6 suggested by the instrument manufacturer to convert Babs into EBC.
Mass Absorption Coefficient

## Slide 49
Chart: Ratio Black Carbon / BC Total
Ratio BC Fine and Coarse Mode to Total BC (2008-2012)